## Slide 1
ECHOMESH
Tactical Acoustic Intelligence for Autonomous Drone Swarms
Detect · Localize · Dominate
Junction DefenceHack · Kova Labs Challenge
Transmission · Mesh · Application

## Slide 2
The Problem
Drones can fly autonomously.
But can they hear the battlefield?
A single UAV may detect an acoustic signature — a gunshot, a missile launch, a tank — but it cannot locate the source alone. You need cross-referencing. You need a mesh.
No source localization
A single sensor detects events but cannot pinpoint origin — triangulation requires multiple synchronized receivers.
Millisecond timing matters
TDOA accuracy depends on sub-millisecond clock sync across drones. Off-the-shelf comms fail here.
Contested RF environments
Jamming and spoofing degrade command links. The mesh must survive partial node loss autonomously.

## Slide 3
Our Solution
A full-stack tactical acoustic intelligence system — built across all three challenge layers
01
TRANSMISSION
Low-latency drone-to-drone data links over raw IEEE 802.11 frames.
Nanosecond-accurate timestamp exchange enables TDOA math.
02
MESH
Multi-drone self-organizing topology with self-healing routing.
Synchronized detections from 3+ nodes gate the triangulation pipeline.
03
APPLICATION
Acoustic threat classification (gunshots, missiles, drones, tanks) combined with TDOA localization and Monte Carlo confidence zones.
Each layer builds on the one below — from raw radio frames to actionable battlefield intelligence.

## Slide 4
System Architecture
Drone Sensors
3+ UAVs
Microphone arrays
Audio Detection
Sliding window
22kHz classifier
Mesh Exchange
events.json
per-drone timestamps
TDOA Solver
Grid search +
Levenberg-Marquardt
Tactical UI
WebSocket map
CEP95 confidence zone
Key Engineering Decisions
Nanosecond timestamp precision
Subtract min timestamp as integer before float conversion — avoids float64 precision loss at ~1.78×10¹⁸ ns.
Grid-then-polish TDOA solver
Coarse 120×120 global search prevents hyperbola branch ambiguity, then LM refines to sub-metre accuracy.
Per-drone error propagation
Each drone's clock σ (ns) and position σ (m) feed Monte Carlo separately, scaling with sensor quality.

## Slide 5
Application: Acoustic Threat Detection
Every drone continuously classifies audio for battlefield-relevant events — 0.5 s windows, 22 kHz
GUNSHOT
▸ Crest factor > 8×
▸ Sub-100 ms impulse
▸ Spectral peak 1–8 kHz
▸ Backfire suppression
MISSILE LAUNCH
▸ Sustained energy burst
▸ Low-freq rumble < 500 Hz
▸ Duration 0.5–3 s
▸ Rising spectral envelope
ENEMY DRONE
▸ Rotor harmonic detection
▸ Blade-pass frequency ISO
▸ Own-rotor notch filter
▸ Spectral subtraction
TANK / VEHICLE
▸ Engine harmonic matching
▸ Heavy low-end energy
▸ Ground vibration profile
▸ Long duration filter
Domain heuristics filter false positives: bird calls vs. gunshots, own rotors vs. enemy UAVs

## Slide 6
Application: TDOA Source Localization
3+ drones detect the same event. Time-difference-of-arrival reveals where the sound came from.
Algorithm
1
Coarse grid search
120×120 global grid minimises TDOA residuals. Prevents hyperbola branch ambiguity — a classic TDOA failure mode.
2
Levenberg-Marquardt polish
Non-linear least-squares refinement from coarse seed. Converges to sub-metre accuracy in contested geometry.
3
Monte Carlo uncertainty
400 samples perturbing drone timestamps (±σ ns) and positions (±σ m). Outputs CEP50, CEP95, GDOP.
Output Metrics
CEP50
50th-percentile radius — half of solutions inside
CEP95
95th-percentile radius — military accuracy standard
GDOP
Geometric Dilution of Precision — mesh geometry quality
WGS84
Output in lat/lon + local metric plane (equirectangular)

## Slide 7
Mesh Layer: Multi-Drone Coordination
Resilient, self-organizing topology — no base station required
✈
DRONE A
✈
DRONE B
✈
DRONE C
HQ
Key Properties
IEEE 802.11 packet injection
Raw frames bypass infrastructure. Works without base stations or internet in fully contested environments.
Nanosecond event timestamps
Each detection tagged with ns-precision timestamp; integer precision preserved for TDOA accuracy.
≥3 node synchronization gate
Pipeline validates and rejects event groups with fewer than 3 synchronized detections — no false localizations.
Self-healing topology
Mesh re-routes around jammed or lost nodes. Partial coverage degrades gracefully rather than failing hard.

## Slide 8
Tactical Command Interface
Real-time situational awareness, streamed via WebSocket at 30 Hz
▸ Drone swarm positions — live telemetry
▸ Detected targets: type, confidence, bearing
▸ TDOA-localized source coordinates (WGS84)
▸ CEP95 confidence ellipse overlay on map
▸ Threat alert log with timestamps
▸ Mesh health and node status panel
ECHOMESH // TACTICAL OPERATIONS
★
TGTS
GUN
UAV
TNK
ALRT
⚠
⚠
●
DRONES: 3/3 ONLINE ● THREATS: 2 ● MESH: HEALTHY

## Slide 9
Results & Capabilities
4
Threat Classes
Gunshot · Missile · Drone · Tank
3+
Drone Mesh
Minimum nodes for TDOA triangulation
400
MC Samples
Per-event uncertainty propagation
What It Delivers
Sub-metre localization accuracy
Grid + LM solver converges to <1 m with good drone geometry (low GDOP); degrades gracefully at high GDOP.
Military-standard confidence reporting
CEP50 and CEP95 radii, 95% confidence ellipse fitted via χ² quantile — directly compatible with C2 integration.
Robust false-positive suppression
Domain heuristics separate real threats from bird calls, wind noise, and own-rotor signatures before any alert fires.

## Slide 10
Why EchoMesh?
Acoustic intelligence is the missing layer in autonomous drone warfare.
▸ Cameras go blind in smoke, darkness, and clutter — acoustic sensors don't.
▸ TDOA localization works without GPS, critical in GPS-denied environments.
▸ More drones = better geometry = higher accuracy. The mesh is the sensor.
▸ Open architecture: swap any classifier, any output format, any C2 interface.
Built at Junction DefenceHack · Kova Labs Challenge
ECHOMESH